Oil, Solids, and Chemical Waste Tanks

ENGINEER SPECIFICATION GUIDE

Striem provides the specification language below to assist in the specification of our products, including oil separators, solids interceptors, chemical waste tanks, and monitoring solutions.

NOTES:

Black: Insert directly into project specification Section 22 40 00 - Plumbing Fixtures or where appropriate.

Blue: Included in this document to assist you and is not to be included in the specification language.

Red: Optional accessories or equipment applicable to the product and available to specify at your discretion.

PART 1 - GENERAL

Insert the following paragraphs under “Submittals”:

A.	Review Submittals:

1.	Product Data: Manufacturer’s standard data sheets describing components including materials, dimensions, relationship to adjacent construction, and attachments.

PART 2 - PRODUCTS

Insert the following under “Manufacturers”. Edit to indicate whether or not substitutions will be permitted for the products in this section.

A.	Contract Documents are based on products by Striem, Kansas City, KS USA

B.	Substitutions: [Under provisions of Division 01.] [Not permitted.]

Insert the following under “Components.” Refer to the Striem catalog or website for part numbers (Please refer to the website for the latest/most up-to-date part numbers and specifications), then select and edit the following paragraphs accordingly. All red text represents optional items, include as necessary.

OIL SEPARATORS

Include the following for an oil separator for all applications – indoor or outdoor, above or below grade.

A.	Oil Separator:

1.	Model: Oil Reserve™ Series Model No. OS-15, OS-25, OS-35, OS-50, OS-75, OS-100, OS-500, OS-750, OS-1000, OS-1500

2.	Description: Striem Oil Reserve™ oil/sand separator model # ____ shall be lifetime guaranteed and made in USA of seamless, rotationally-molded Polyethylene with minimum 3/8” uniform wall thickness. Separator shall be furnished for above or below grade installation, with field adjustable riser system, built-in flow control and vent connections. Separator flow rate shall be ____ GPM. Separator capacity shall be ____ gallons of oil and ____ gallons of sediment. Cover shall provide water/gas-tight seal and have minimum ____ lbs load capacity. Optional: Add Clean Sweep™ oil coalescing media for effluent quality of 5ppm (mg/L) oil content for models OS-35, OS-50, OS-75, OS-100, OS-750, OS-1000, OS-1500.

Include the following for an oil separator with oil level monitoring, for all applications – indoor or outdoor, above or below grade.

A.	Oil Separator with oil level monitoring:

1.	Model: Slick Stick™ Oil Level Monitoring System. OS-50-SS, OS-75-SS, OS-100-SS, OS-500-SS, OS-750-SS, OS-1000-SS, OS-1500-SS

2.	Description: Striem Slick Stick™ oil level monitoring system model # ____ shall be lifetime guaranteed and made in the USA of seamless, rotationally-molded Polyethylene with minimum 3/8” uniform wall thickness. Separator shall be furnished for above or below grade installation, with field adjustable riser system and vent connections. Separator capacity shall be ____ gallons of oil and ____ gallons of sediment. Cover shall provide water/gas-tight seal and have minimum ____ lbs load capacity.

SOLIDS INTERCEPTORS

Include the following for a solids interceptor for indoor, point-of-use or in-line drainage (versus surface drainage) applications, including application for hair/lint/food waste/sand/sediment/industrial debris.

A.	Interceptor:

1.	Model: HLT(or B) Series Model HLT(or B)-1176-X

2.	Description: Striem solids interceptor model #____ shall be lifetime guaranteed and made in USA of seamless, rotationally-molded Polyethylene with minimum 3/8” uniform wall thickness. Interceptor shall be furnished with removable 304 series stainless steel basket. Interceptor shall be watertight up to 36” head and contain internal sewer gas trap. Interceptor shall have 4” hand-threaded access with gasket.

**** OR ****

A.	Interceptor:

1.	Model: USI Series Model USI-1180-X, USI-1184-X

2.	Description: Striem solids interceptor model #____ shall be lifetime guaranteed and made in USA of seamless, rotationally-molded Polyethylene with minimum 3/8” uniform wall thickness and removable polyethylene bucket and filter. Interceptor shall be watertight up to 36” head and contain internal sewer gas trap. Interceptor shall have cover with gasket and hand thread clamps.

Include the following for a solids interceptor for all in-line drainage (versus surface drainage) applications – indoor or outdoor, above or below grade, including applications for food waste from disposers, hair, lint, etc.

A.	Interceptor:

1.	Model: Aardvark™ Series Model AA-S

2.	Striem Aardvark™ solids interceptor model AA-S shall be lifetime guaranteed and made in the USA. Tank material shall be polyethylene. Interceptor shall have removable, corrosion-resistant filter basket. Interceptor shall be equipped with high and low outlet options, with a movable sewer gas trap to be located on either outlet. Interceptor shall be furnished for above- or below-grade burial. Cover shall be water and gas tight with a minimum 450 lbs. load capacity, or 2,500 lbs capacity when buried with a riser. Interceptor shall be in compliance with IAPMO IGC 167-2011ae2.

A.	Interceptor:

1.	Model: Aardvark™ Series Model AA-M, AA-L or AA-XL

2.	Striem Aardvark™ solids interceptor model ______ shall be lifetime guaranteed and made in the USA. Tank material shall be polyethylene. Interceptor shall have removable, corrosion-resistant filter basket. Interceptor shall be equipped with high and low outlet options, with a movable sewer gas trap to be located on either outlet. Interceptor shall be furnished for above- or below-grade burial. Cover shall be water and gas tight with a minimum ______ lbs. load capacity. Interceptor shall be in compliance with IAPMO IGC 167-2011ae2.

**** OR ****

A.	Interceptor:

1.	Model: Prospector™ Series Model PS-15-S, PS-25-S, PS-35-S, PS-50-S, PS-125-S or PS-275-S

2.	Description: Striem Prospector™ solids interceptor model # _____ shall be lifetime guaranteed and made in USA of seamless, rotationally-molded Polyethylene with minimum 3/8” uniform wall thickness. Interceptor shall be furnished for above or below-grade installation. Interceptor shall be furnished with screen and connection for extending handle to grade for deep burials. Cover shall provide water/gas-tight seal and have a minimum _____ lbs load capacity.

Include the following for a solids interceptor for all surface drainage (versus in-line drainage) applications – indoor or outdoor, below grade, including application for sand/oil, parking lots, carwashes, and other interception of surface drainage debris.

A.	Interceptor:

1.	Model: Settler™ Series Model CB-50-S, CB-125-S or CB-275-S

2.	Description: Striem Settler™ catch basin model # _____ shall be lifetime guaranteed and made in USA of seamless, rotationally-molded Polyethylene with minimum 3/8” uniform wall thickness. Interceptor shall be furnished for below-grade installation with highway-rated gasketed, solid composite cover. Interceptor shall be provided with inlet and outlet connection.

**** OR ****

A.	Interceptor:

1.	Model: Settler™ Series Model CB-50-G or CB-125-G

2.	Description: Striem Settler™ catch basin model # _____ shall be lifetime guaranteed and made in USA of seamless, rotationally-molded Polyethylene with minimum 3/8” uniform wall thickness. Interceptor shall be furnished for below-grade installation with a pickable, H20 highway-rated cast iron grate. Interceptor shall be provided with outlet connection and capped optional inlet connection.

Optional: Add BCB-7 removable sediment basket for initial separation.

CHEMICAL WASTE TANKS

Include the following for all indoor, point-of-use acid neutralization tank applications (one tank for each lab station).

A.	Acid Neutralization Tank:

1.	Model: Lab Rat™ Series Model LB-2 or LB-5

2.	Description: Striem Lab Rat™ neutralization tank model # _____ shall be lifetime guaranteed and made in the USA of seamless, rotationally-molded Polyethylene with minimum ¼” uniform wall thickness. Tank shall be furnished with built-in top and side inlet connection options, field-adaptable for 1-1/2” or 2” drain line pipe size. Tank shall be watertight up to 36” head and contain an internal sewer gas trap. Tank shall have gasketed cover with captive, hand-thread hardware.

Optional: Use Striem limestone chips 2” - 3” in size with a calcium carbonate content (CACO3) of 90% or greater.

Include the following for any acid neutralization tank applications, indoor or outdoor, above or below grade, including application for professional and teaching labs up to 75 lab stations (sinks) or 250 gallons liquid capacity, and industrial process neutralization.

A.	Acid Neutralization Tank:

1.	Model: Lab Basin™ Series Model LB-15, LB-25, LB-35, LB-50, LB-125 or LB-275

2.	Description: Striem Lab Basin™ neutralization tank model # ______ shall be lifetime guaranteed and made in USA of seamless, rotationally-molded Polyethylene with minimum 3/8” uniform wall thickness. Tank shall be furnished with inlet, outlet, vent, cover(s), riser system, monitoring equipment and other modifications per jobsite-specific conditions and per engineer’s specification.  Cover shall provide water/gas-tight seal and have a minimum ______ lbs load capacity.

Optional: Use Striem limestone chips 2” - 3” in size with a calcium carbonate content (CACO3) of 90% or greater.

Include the following for any acid neutralization tank applications, indoor or outdoor, below grade (direct bury), including applications for professional and teaching labs from 8 - 500 lab stations (sinks) or 1,500 gallons liquid capacity, and industrial process neutralization.

A.	Acid Neutralization Tank:

1.	Model: NT Series Model NT-XX-B.

2.	Description Striem NT Series neutralization tank model # _____ shall be lifetime guaranteed and made in USA of seamless, rotationally-molded Polyethylene with minimum 3/8” uniform wall thickness. Tank shall be furnished with inlet, outlet, vent, cover(s), bracing, field adjustable riser system, monitoring equipment and other modifications per jobsite-specific conditions and per engineer’s specification.  Cover shall provide water/gas-tight seal and have a minimum 16,000 lbs load capacity.

Optional: Use Striem limestone chips 2” - 3” in size with a calcium carbonate content (CACO3) of 90% or greater.

Include the following for any acid neutralization tank applications, indoor or outdoor, above grade, including applications for professional and teaching labs from 8 - 500 lab stations (sinks) or 1,500 gallons liquid capacity, and industrial process neutralization.

A.	Acid Neutralization Tank:

1.	Model: NT Series Model NT-XX-A.

2.	Description Striem NT Series neutralization tank model # _____ shall be lifetime guaranteed and made in USA of seamless, rotationally-molded Polyethylene with minimum 3/8” uniform wall thickness. Tank shall be furnished with inlet, outlet, vent, cover(s), monitoring equipment and other modifications per jobsite-specific conditions and per engineer’s specification.

Optional: Use Striem limestone chips 2” - 3” in size with a calcium carbonate content (CACO3) of 90% or greater.

Include the following for monitoring the pH of any waste stream or tank with one pH sensor, including acid waste lines in teaching and professional labs and industrial process. Command Center™ includes one pH sensor, monitoring/alarm panel, 50ft of sensor wire and a sensor cleaning and calibrating kit. Sensor placement kits (SPKs) for installing the pH sensor above or below grade are required, but sold separately.

A.	pH Monitoring System

1.	Model: Command Center™ Model: CC-1

2.	Description: BMS compatible via an ethernet port, color touch screen pH recorder/controller furnished with 2.5 years of recording memory, audio and visual alarms, preprogrammed and ‘ready to use’ with high and low pH set points and logic to flush outlet line with fresh water as pH approaches high and low set points (solenoid and piping by others), pH sensor maintenance kit containing sensor cleaning brush and solution, and calibration buffer solutions, NEMA 4X lockable enclosure, fully UL listed components. Sensor placement kit for above (SPK-A) and below (SPK-B) grade installations.

Include the following for any decontamination holding tank applications, indoor or outdoor, above or below grade, including application for emergency wash down stations, battery changing stations, and industrial process surface drainage.

A.	Decontamination Holding Tank:

1.	Model: Bio Basin™ Series Model BB-275, BB-500-B, BB-750, BB-1000 or BB-1500

2.	Description: Striem Bio Basin™ decontamination tank model # ______ shall be lifetime guaranteed and made in USA of seamless, rotationally-molded Polyethylene with minimum 3/8” uniform wall thickness. Tank shall be furnished with inlet, outlet, vent, cover(s), riser system, monitoring equipment and other modifications per jobsite-specific conditions and per engineer’s specification.  Cover shall provide water/gas-tight seal and have a minimum 16,000 lbs load capacity.

Optional: add a single (AVA-3) or multi-level (AVA-4) float switch and alarm panel, and optional manual or electronic valves.

SAMPLING PORTS

Include the following anywhere visual or sampling access is required to monitor effluent water quality before entering the public sewer system.

A.	Sampling Port:

1.	Model: Sewer Viewer™ Series Model SV4-XX or SV24-XX

2.	Description: Sewer Viewer™ sampling port model #______ shall be manufactured by Striem, Kansas City, KS. Port shall be lifetime guaranteed and made in USA of seamless, rotationally molded Polyethylene with minimum 3/8” uniform wall thickness. Port shall be built in accordance with the Water Environment Federation’s “Standard methods for Examination of Water and Wastewater” with sealed top access port and highway rated composite cover and TeleGlide™ field adjustable riser as required when buried.

PART 3 - EXECUTION

Include the following under “Installation”:

A.	Install components in accordance with manufacturer's instructions and approved product data submittals.